| Contractor |  | Date |  | Review No |  |
| --- | --- | --- | --- | --- | --- |
| Contract No. |  | Project No. |  | Project Name |  |

| Reference | Requirement | Addressed | Comment |
| --- | --- | --- | --- |
| MRTS07A Cl 5.2 | Has the Contractor prepared documented procedures for all construction processes? |  |  |
| MRTS07A Clause 1 Annexure | What stabilizing agent is to be used and at what rate (content)? |  |  |
| MRTS07A Cl 6.1 & 7.2 | Does any additional material which is required to be incorporated comply with the requirements and standards stated in Clause 2 of the Annexure MRTSO7A.1 |  |  |
|  | Has the area to be treated been identified and marked |  |  |
| MRTS07A Cl 6.2 Cl 8.1.3.3 | Has the type of admixture been approved by the Administrator and the content approved in writing? |  |  |
| MRTS07A Cl 6.3 | Is water free from oil, acids, organic matter and other matter which could be deleterious to the mixture? |  |  |
| MRTS07A Cl 8.3.2 | Has a trial section been carried out for each particular type of in situ stabilisation treatment in accordance with the specification? |  |  |
| MRTS07A Cl 8.4.2 | Has any additional material required for shape correction been spread onto the surface of the pavement and trimmed to a shape suitable for stabilising and trimming to the heights and shapes shown on the Drawings? |  |  |
| MRTS07A Cl 8.4.6 | Has the stabilising agent been uniformly spread across the in situ material? |  |  |
| MRTS07A Cl 8.4.5? | If the stabilising agent is lime, has it been lightly watered to prevent any loss due to wind action? |  |  |
| MRTS07A Cl 8.4.9 | After completion of stabilisation and before compaction, has the surface been trimmed to approximately the shapes specified and have any depressions been filled with mixed material? |  |  |
| MRTS07A Cl 8.1.4 & Clause 8 of the Annexure MRTS07A.1 | Has compaction occurred within the time limit set down in the specification? |  |  |
| MRTS07A Cl 8.4.14 | Has the curing operation commenced immediately after the completion of compaction and in accordance with the specification? |  |  |
|  | Is the finished surface tight and matching existing surfaces? |  |  |
| MRTS07A Cl 8.4.5? | Has the area treated been proof rolled? |  |  |
| MRTS07A Cl 9.7? | Have final dimensions been checked in accordance with specification? |  |  |
| MRTS07A Cl 8.5.5 | Does the surface evenness of the final pavement meet specification? |  |  |
| MRTS07A Cl 9.2 | Has compliance testing of the pavement been undertaken for each lot? |  |  |
|  | Has suitable signage been erected? |  |  |

Additional Issues for consideration

| Reviewed By: |  |  |  |  | / / |
| --- | --- | --- | --- | --- | --- |
|  | Name |  | Signature |  | Date |