| Contractor |  | Date |  | Review No |  |
| --- | --- | --- | --- | --- | --- |
| Contract No. |  | Project No. |  | Project Name |  |

| Reference | Requirement | Addressed | Comment |
| --- | --- | --- | --- |
| MRTS03 Cl 12.3.5 MRTS04 Cl 13 Cl 9 | Excavation, foundation and bedding Has it been ensured that the width of excavation is no greater than specified? Have unsuitable materials been identified, removed and replaced? Does bedding provide continuous even support? Is bedding under each spigot greater than 50 mm? |  |  |
| MRTS03 Cl 15 | Has the foundation/bedding material been compacted to achieve the specified compaction standard? |  |  |
| MRTS03 Cl 12.2 | Have the correct bandage covers been used? Hold Point 1 |  |  |
| MRTS03 Cl 7 | Has the contractor installed the culvert components to the horizontal and vertical tolerances specified? |  |  |
| MRTS03 Cl 12.3.2 MRTS04 Cl 19 | Does the haunch, side and overlay material conform to the required specifications? Has the backfill been placed and compacted uniformly in layers? Has the side and overlay zone been compacted to the specified requirements? |  |  |
| Std Drawings 1359 | For multiple cell culverts do the spacing between the culverts comply with the specified requirements? |  |  |
| Std Drawings 1304, 1305. 1306 | Check formwork is sufficient for concrete pour loads. Have the end structures been constructed in accordance with the relevant specifications? |  |  |
| MRTS04 Cl 5.4 | Compliance testing: Have the geometric tolerances been checked at the points nominated in the specification? Is the compaction standard for each lot represented by the characteristic value of the RDD’s? |  |  |

Additional Issues for consideration

|  | Sealing penetrations of pre-cast headwalls should be from the back of the headwall to prevent blowout of sealing material |
| --- | --- |
|  | Pre-cast headwalls for multi-cell culvert extensions require additional effort by manufacture to match existing culvert spacing which may not be in accordance with Standard Drawing. |

| Reviewed By: |  |  |  |  | / / |
| --- | --- | --- | --- | --- | --- |
|  | Name |  | Signature |  | Date |